## Slide 1
INTELLIGENT IoT-DRIVEN
Gas Leak Detection
with Multi-Layered Automated Protection
Layer 1
Sensing
Layer 2
Processing
Layer 3
Actuation
Layer 4
Communication
Layer 5
Recovery
MQ-2/MQ-6 · ESP32 · LM35 · Solenoid Valve · Buzzer · Exhaust Fan · GSM Module
System Architecture · 5-Layer Design

## Slide 2
1
Layer 1 — Sensing
Physical environment monitoring
MQ-2 / MQ-6
Gas Sensor
Detects LPG, propane, methane
Analog output → ADC on ESP32
Fast response time
Calibrated PPM threshold
LM35
Temperature Sensor
Precision analog temp sensor
10 mV/°C output
No external calibration needed
Feeds ESP32 ADC directly

## Slide 3
2
Layer 2 — Processing (ESP32)
Pre-ignition detection, threshold logic, decision making
ADC / Analog Read
PPM Calculation
12-bit ADC on ESP32
Reads MQ-2/MQ-6 & LM35
Converts voltage → PPM
Polling at configurable interval
Threshold Comparator
Gas + Temp Logic
Configurable PPM limit
Temperature upper bound check
Combined logic gate (AND/OR)
Triggers alert condition
Event State Machine
IDLE → ALERT → SAFE
Three-state FSM on ESP32
IDLE: monitoring, no action
ALERT: actuation + notify
SAFE: post-clearance reset
Core intelligence runs entirely on-chip — no cloud dependency for actuation decisions.

## Slide 4
3
Layer 3 — Actuation
Multi-layer protection — Automated physical responses
Solenoid Valve
Gas Cutoff
Normally-closed (fail-safe)
Inverse logic: closes on trigger
Power-loss = valve closes
Relay-isolated from ESP32
Exhaust Fan
Ventilation
Activated on ALERT state
Clears gas from enclosure
High-current motor via relay
Auto-off after clearance
Buzzer
Local Alarm
Piezo buzzer on GPIO
Audible alert to occupants
Pulse pattern on ALERT
Silences on SAFE state

## Slide 5
4
Layer 4 — Communication & Alert
Remote notification and connectivity
GSM Module
SIM800 / SIM900 — SMS Alert to User
SMS alert to registered number on ALERT state
Works without internet or Wi-Fi connection
AT command interface via UART on ESP32
Backup power supply recommended
Configurable recipient list in firmware
GSM Coverage
Why GSM Only?
Cellular network — no local infrastructure needed
Reliable in power outage scenarios
SIM800/900 widely available & low cost
Sufficient for life-safety notification
Wi-Fi & Telegram excluded from this build

## Slide 6
5
Layer 5 — Recovery & Safety Reset
System returns to safe state after gas clearance is confirmed
Gas Level Polling
Below Threshold?
Continuous PPM monitoring
Compares against safe threshold
Must be sustained, not transient
Triggers recovery sequence
Valve Re-Open
Manual Reset Only
Operator must physically confirm
No automatic re-open after alert
Prevents premature gas restore
Button / switch input on ESP32
Fan Auto-Off
Clearance Confirmed
Fan stops after PPM drops
Automatic — no manual action
Confirmation logged in FSM
System transitions to SAFE
Safety-critical constraints: Entire circuit insulated — no exposed sparks near gas. Solenoid uses inverse logic (fail-safe: closed on power loss). 3.3 V / 5 V separation via relay isolation.