## Slide 1
IoT Gas Leak Detection System
Proof of Concepts
Intelligent IoT-Driven Gas Leak Detection
with Multi-Layered Automated Protection
POC 1
Data Validation
POC 2
Control Logic
POC 3
Communication

## Slide 2
POC 1 — Data Validation
MQ-6 · LM35 · ESP32
Objective
Verify that the MQ-6 and LM35 sensors produce accurate readings, and that the ESP32 threshold logic correctly transitions from IDLE to ALERT when gas or temperature exceeds the safe limit.
Hardware Connections
MQ-6 AOUT → ESP32 GPIO34 (ADC1_CH6) | VCC → 5V
LM35 output → ESP32 GPIO35 (ADC1_CH7) | VCC → 3.3V
Serial monitor at 115200 baud for live PPM and °C output
Test Steps
Power on — allow 60s warm-up before readings are valid
Check baseline: PPM < 300 ppm in clean air, temp ~25°C
Introduce LPG near sensor — confirm PPM rises on serial monitor
Verify ALERT state triggers when PPM crosses 500 ppm
Key Parameters
ADC
12-bit, 0–3.3V
PPM
Vcurrent / Vclean × ref
LM35
10 mV / °C
Gas threshold
500 ppm
Temp threshold
55 °C
Pass Criteria
PPM rises measurably when gas is introduced
ALERT triggers reliably at 500 ppm threshold
No false triggers in 10-min clean-air test
State Machine
IDLE
ALERT
SAFE

## Slide 3
POC 2 — Control Logic
ESP32 · Solenoid Valve (manual shutoff) · Relay · Exhaust Fan · Buzzer
Objective
Verify that the ESP32 simultaneously activates the exhaust fan (via relay) and buzzer on ALERT. Fan turns off automatically through code once PPM drops below threshold. Solenoid valve is shut off manually.
Hardware Connections
ESP32 GPIO5 → Relay IN → Exhaust Fan (MF40100V1) | Fan on 12V rail
ESP32 GPIO19 → Piezo Buzzer (CEM-1203)
Solenoid valve connected to gas cylinder — manually turned off on leak
Test Steps
Simulate ALERT — exhaust fan starts via relay, buzzer sounds simultaneously
Confirm both fire within the same ESP32 polling cycle
Simulate gas clearing — PPM drops below threshold in code
Confirm fan turns OFF automatically and buzzer stops — no physical button needed
Key Parameters
Fan control
Relay — 5V coil, 12V load
Fan off
Code — PPM < threshold
Buzzer
GPIO19 direct drive
Valve shutoff
Manual by user
Relay — Why Here?
The exhaust fan runs on a 12V DC motor — too much current and voltage for the ESP32 GPIO (max 3.3V / 12mA) to drive directly. The relay acts as a switch: ESP32 controls the low-power coil side, and the relay switches the high-current fan circuit safely.
Pass Criteria
Fan and buzzer fire simultaneously on ALERT
Fan turns off automatically when PPM clears in code

## Slide 4
POC 3 — Communication
ESP32 · GSM SIM800L / SIM900A · UART · AT Commands · SMS
Objective
Verify that the ESP32 sends an SMS alert to the user's phone via the GSM module on ALERT, using UART communication and AT commands — with no internet or Wi-Fi required.
Hardware Connections
ESP32 TX (GPIO17) → GSM RX | ESP32 RX (GPIO16) → GSM TX (Serial2)
GSM powered from dedicated 4.2V / 2A supply — not from ESP32
AT Command Sequence
AT → expect OK
AT+CMGF=1 → set SMS text mode
AT+CMGS="+91XXXXXXXXXX" → enter phone number
"GAS ALERT! Leak detected. Check immediately." → send 0x1A
Key Parameters
UART port
Serial2 — GPIO16/17
Baud rate
9600 bps
SMS mode
AT+CMGF=1 (text)
Network
2G GSM — no internet
Communication Flow
ESP32
→
GSM
→
Phone
Pass Criteria
SMS delivered within 10 seconds of ALERT trigger
Message content correct and readable
No missed alerts across 5 consecutive trigger tests

## Slide 5
Integration Roadmap
1
Phase 1
POC 1 — Data Validation
MQ-6 + LM35 → ESP32 ADC → Serial monitor. No actuators. Validate sensor readings and IDLE → ALERT threshold logic.
Standalone
2
Phase 2
POC 2 — Control Logic
ESP32 → Relay → Exhaust Fan + Buzzer. Triggered manually. Fan turns off via code when PPM clears. Solenoid valve shut off manually.
Standalone
3
Phase 3
POC 3 — Communication
ESP32 → GSM SIM800/900A. Triggered manually. Validate UART link and SMS delivery across 5 consecutive tests.
Standalone
4
Phase 4
Full System Integration
All 3 POCs combined. Sensor triggers fan + buzzer + SMS simultaneously. Full test with real gas introduction.
Integration